## Slide 1
[Helium leak test machine (WGR) ]
P1
dB
Chamber 1
Chamber 2
Trigger recording time
8:00 AM and 20:00PM every day
Feature
Transfer data from DB to Excel file which using form designed
in c:\radiator\master\Calibratehelium.xlsx (depend on setting)
2. File is created on section-name if system has more one section-code
3. Provide Function re-update on datetime by individual.
Understand Outline
Calibration time is 23:00 PM yesterday - 08:00 AM today => Shift = Day (D)
Calibration time is 11:00 AM today - 20:00 PM today => Shift = Night (N)
Using latest only. One day has 2 times.
Operation manual Auto Recording software
Collaborate Lab
Make sure software
running all time.
Understand Condition

## Slide 2
Understand Flow Chart
P2
Raw Data
Normal Data
Service
Software 1
Service
Software 2
Master File (Excel)
OUTPUT
Excel Files
: Schedule Trigger
ST
ST
: Run all time on BPK. Server.
A
B
ST
8:00 AM,20:00PM
8:02 AM,20:02PM
read
insert
read
copy
write
: Run all time on each individual
or on demand.
Individual section
Need
Setup directory
Need
Setup directory
Operation manual Auto Recording software
Collaborate Lab

## Slide 3
Understand Folder structure
C:\Radiator\Assy1\Calibratehelium_1_June’21.xlsx
C:\Radiator\master\Calibratehelium.xlsx
File Master
Fixed folder
Year
Month
Chamber no.
Filename
Section name
Auto Record folder
P3
Operation manual Auto Recording software
Collaborate Lab

## Slide 4
Understand File Master
Do NOT change sheet name
Auto filling.
Do NOT touch this area.
P4
Operation manual Auto Recording software
Collaborate Lab

## Slide 5
Understand File recorded
File name
Recorded data : data is transferred 2 Chamber
On Day-shift and Night-shift twice.
P5
Operation manual Auto Recording software
Collaborate Lab

## Slide 6
Understand Service software
Run file Service.exe
Program create file C:\KPi\Login\Connection.dat
Network 3G/4G/5G :4G,Local
Network Local : Local,4G
You should select connection type
And Program create file C:\KPi\AutoRecord\Recording.txt
You make sure subdirectory to keep file. You can change by yourselves.
Such as “D:\RadiatorAssy” instead. And SAVE File.
If you edit file, you should restart this program again to create new folder.
P6
Operation manual Auto Recording software
Collaborate Lab

## Slide 7
In the case:
Don’t edit data
In the case:
Change to D:\RadiatorAssy
P7
Bring Calibratehelium.xlsx file to place at “Master” folder
of “Radiator” folder or “RadiatorAssy” folder.
2. Run file Service.exe again. (In the case : RadiatorAssy)
Trial save transfer data by individua.
Step I: select start & stop date
Step II: push Helium start
Step III: Excel file and section-name folder
is created at Radiator directory . It has 2 files.
If these files lost. It created after trigger running.
But data is NOT full, should update by self.
Operation manual Auto Recording software
Collaborate Lab
Understand Service software

## Slide 8
P8
Data in database.
After data was transferred.
Operation manual Auto Recording software
END
Collaborate Lab
Understand Service software

## Slide 9
Appendix
2021-07-01 D
2021-07-01 N
2021-07-02 D
2021-07-02 N
2021-07-05 N
2021-07-06 D
WGR].[dbo].[RD_HL_CalibrationTable] (Before)
WGR].[dbo].[RD_HL_Calibration] (After)
Calibration time is 23:00 PM yesterday - 08:00 AM today => Shift = Day (D)
Calibration time is 11:00 AM today - 20:00 PM today => Shift = Night (N)
Condition